## Slide 1: Analytical Method for First Order Rayleigh Scattering in CBCT Application
PHYS 4250 Project report
Yutong Zhao

## Slide 2: Computed Tomography (CT) & Cone beam CT (CBCT)
CT: 2-D Picture CBCT:3-D Structure
Notes: Introduce CT and Cone beam CT.
CT is widely used in medical physics.
CT ‘s fundamental principle
CBCT can save time and increase efficiency

## Slide 3: Medical Imaging System
Application:
Image Guided Radiotherapy
(figure)
Tumor & Trauma Diagnosis
Nondestructive testing
Notes: Some application of CBCT.
1,2,3
Our focus is on Image guided radiotherapy

## Slide 4: Motivation
Scatter correction in CBCT provide better anatomical image quality.
Notes: The purpose of this project. ----- Calculate scatter and improve image quality.

## Slide 5: Current problem
Scattering induced noise[1]
Campton scattering
(solved)
Rayleigh scattering
(remain to be solved)
X-ray source
X-ray source
Water
Water
“Lower Scatter condition”
“Higher Scatter condition”
Notes: Figure:
1. The darker of the image, the low resolution we have.
2. The larger the divergence angle, the low resolution in center.
Large angle – larger scan volume
Scattering contains two parts. --------concentrate on Rayleigh.

## Slide 6: Radiation Interaction
Rayleigh scattering
Energy range
KV-range
Notes: Figure:
The photon interaction in matter. (water)
Rayleigh scattering range ---- X-ray source
Don’t forget attenuation (latter)

## Slide 7: Rayleigh Scattering[2]
Scattering theory:
Detected Signal
X-ray Intensity
Differential
Cross section
Solid angle
of detector
Notes: N_s expected signal

## Slide 8: Differential Cross Section
Transfered momentum: (in unit )
Constant
Material Form Factors[2]
Atomic Form Factors [3]
Chemical composite
Notes: r0------- classical electron radius
W------ molecule weight
Wi------ mass fraction of i
Mi------ atomic mass of i
Atomic form factors ---- describe the shape of atom according to atomic number

## Slide 9: Atomic Form Factors
Notes: Spline Interplotation
Size of atoms
With atomic number increase, shape increase

## Slide 10: Material Chemical Formulas (EGS data)
Human tissue/(mass fraction) |  | Water | Human Lung | Human Bone
Elements | Density) | 1.0 | 0.26 | 1.85
H |  | 0.112 | 0.103 | 0.063984
C |  | ----- | 0.105 | 0.278
N |  | ----- | 0.031 | 0.027
O |  | 0.888 | 0.749 | 0.410016
Na |  | ----- | 0.002 | -----
Mg |  | ----- | ----- | 0.002
P |  | ----- | 0.002 | 0.07
S |  | ----- | 0.003 | 0.002
Cl |  | ----- | 0.003 | -----
K |  | ----- | 0.002 | -----
Ca |  | ----- | ------ | 0.147
Human tissue/(mass fraction) |  | Water | Human Lung | Human Bone
Elements |  | 1.0 | 0.26 | 1.85
H |  | 0.112 | 0.103 | 0.063984
C |  | ----- | 0.105 | 0.278
N |  | ----- | 0.031 | 0.027
O |  | 0.888 | 0.749 | 0.410016
Na |  | ----- | 0.002 | -----
Mg |  | ----- | ----- | 0.002
P |  | ----- | 0.002 | 0.07
S |  | ----- | 0.003 | 0.002
Cl |  | ----- | 0.003 | -----
K |  | ----- | 0.002 | -----
Ca |  | ----- | ------ | 0.147
Notes: Water & lung very close , different density
Bone --density & composite

## Slide 11: Form Factor interpolation
Database #1
Notes: Water & lung –> very close
Bone -- calcium influence

## Slide 12: Mass attenuation coefficients and interpolation
N0
Nt
KV range
Database #2
Notes: Coherent result:
Water & lung --- close
Bone --- different
All the database we need

## Slide 13: Simulation Setup (Parallel beam Geometry)
Interaction site
Notes: How we determine \theta , trace, and solid angle

## Slide 14: Simulation setup
Notes: Sweep Beam covered volume

## Slide 15: MATLAB code
main_r_1stScatteredFluence.m
Input Constants
Define Geometry
Plot Phantom (3D)
Define X-ray
Load databases
Find Trace
Scatter + Attenuation
Sweep
x,y&z
End

## Slide 16: Verification using Monte-Carlo method
AMCcomparison.m
Monte Carlo simulation
  Modified Dosxyznrc user code (EGSnrc package)
Load Analytical Result
Load M-C Result
Compare
Spectrum difference
Percentage difference

## Slide 17: Simulation phantom (Water)

## Slide 18: Simulation Results (Water)

## Slide 19: Compare with Monte-Carlo Method
Notes: Percentage different – normal distribution

## Slide 20: Simulation phantom (half water half lung)

## Slide 21: Simulation Results

## Slide 22: Compare with Monte-Carlo Method

## Slide 23: Discussion
Limit 1: We do not have experiment data to validate our results.
Limit 2: The X-ray is parallel. We need to generalize to divergent beam.
Limit 3: Only apply to singly scatter.

## Slide 24: Conclusion
1. A reliable analytical method for Rayleigh scattering has been build under parallel beam geometry.
2. Time-saving by utilizing pre-calculations (3.6s compare to 7 hours)
3. Combining with Compton scattering method, the total singly scattered fluence pattern can be obtained.
4. Beneficial to first order scatter correction in CBCT reconstruction

## Slide 25: Questions?
Thank you!

## Slide 26: Reference
[1] J. H. Siewerdsen and D. A. Jaffray, " Cone-beam computed tomography with a at-panel imager: Magnitude and effects of x-ray scatter," Medical physics, vol. 28, no. 2, pp. 220-231, 2001.
[2]. H. Ingleby, J. Lippuner, D. W. Rickey, Y. Li, and I. Elbakri, "Fast analytical scatter estimation using graphics processing units," Journal of X-ray science and technology, vol. 23, no. 2, pp. 119-133, 2015.
[3]. Hubbell, J. H., Veigele, W. J., Briggs, E. A., Brown, R. T., Cromer, D. T., & Howerton, R. J. "Atomic form factors, incoherent scattering functions, and photon scattering cross sections." Journal of physical and chemical reference data vol.4, no.3 pp.471-538,1975.

## Slide 27: Back up pages:

## Slide 28: Complex Phantom (human breast)

## Slide 29: Simulation Results (human breast)

## Slide 30: Future work

## Slide 31: 1st order scatter (Compton & Rayleigh)

## Slide 32: Final Formula:
Total flux :
Cross section:
Radiology pass: